## Slide 1
OCP CHINA · HARDWARE FAULT MANAGEMENT
Hardware Fault Management RAS API
PLDM over MCTP end-to-end demo — OpenBMC (AST2600) ↔ Zephyr (RISC-V), bridged over two live QEMU instances
Requester
OpenBMC pldmd / mctpd — EID 8
Responder
Zephyr serial_bridge — EID 18
Transport
MCTP-over-serial (DSP0253) via unix socket
Result
Auto-discovery + fwd/reverse PLDM (rc=0)
Demo host: internal dev machine · branch RASAPI
Presenter guide: see DEMO_GUIDE.md for the exact step-by-step SSH walkthrough

## Slide 2
OVERVIEW
What we will demonstrate
1
The problem & the RAS API goal
Why HFM needs a standard sensor/effecter transport between a BMC and satellite MCUs
2
Architecture — the four moving pieces
QEMU 11 · Zephyr on RISC-V · I3C model · MCTP+PLDM stack
3
The realized topology
Two QEMU instances bridged over MCTP-serial (DSP0253)
4
Live demo — forward discovery
OpenBMC pldmtool drives PLDM Type 0/2 against Zephyr EID 18
5
Live demo — reverse path (patch 0009)
Zephyr requester → BMC responder, tag-owner bit fix
6
Full auto-discovery — three fixes & wrap-up
kernel busy-loop (0010) + control TO bit (0011) + systemd order (0006)
Hardware Fault Management · RAS API · MCTP/PLDM over QEMU
2

## Slide 3
MOTIVATION
Why a RAS API — and why PLDM over MCTP
The pain point
Large-scale data centers must detect, report and act on hardware faults across thousands of heterogeneous devices.
A BMC needs a vendor-neutral way to:
• discover satellite controllers
• read sensors (temp, voltage, fan)
• read/set thresholds & effecters
• receive async fault events
The DMTF PMCI answer
PLDM (Platform Level Data Model) carried over MCTP (Management Component Transport Protocol).
This demo proves the full stack on emulated hardware:
PLDM Type 0 — base / discovery (DSP0240)
PLDM Type 2 — platform monitoring, PDR & sensors (DSP0248)
MCTP — transport & EID routing (DSP0236)
Hardware Fault Management · RAS API · MCTP/PLDM over QEMU
3

## Slide 4
ARCHITECTURE
The protocol layer stack
App — PLDM Type 0/2 responder (samples/.../serial_bridge)
▼
libpldm — encode/decode (vendored openbmc/libpldm)
▼
libmctp — framing, EID routing (upstream module)
▼
MCTP bindings — serial DSP0253 · I3C DSP0233 · I2C DSP0237
▼
Zephyr UART / I3C driver (upstream)
▼
QEMU 11 machine model (sifive_u / ast2600-evb)
Delivered as numbered patches 0001–0011 under patches/ — full apply order in patches/README.md
Hardware Fault Management · RAS API · MCTP/PLDM over QEMU
4

## Slide 5
ARCHITECTURE
Realized topology — two QEMU instances over MCTP-serial
OpenBMC QEMU
-machine ast2600-evb
pldmd (PLDM Type 0/2 requester)
mctpd (AF_MCTP bus-owner)
kernel mctp-serial driver
EID 8
Zephyr QEMU
-machine sifive_u
serial_bridge sample
PLDM Type 0 + Type 2 responder
MCTP control responder
EID 18
unix socket /tmp/hfm-mctp.sock
OpenBMC = socket server (start first) · Zephyr = client
MCTP link rides each side's SECOND -serial backend (uart1 / ttyS0); the first -serial stays the console.
Hardware Fault Management · RAS API · MCTP/PLDM over QEMU
5

## Slide 6
PREREQUISITES
What is already built on the dev machine
Component
Location / artifact
Verify
QEMU 11.0.0
~/qemu-build/bin/qemu-system-{arm,riscv64}
runs -machine help
OpenBMC image (+0004/6/10)
obmc-phosphor-image-evb-ast2600.static.mtd
md5 9a858c13
Zephyr ELF (+0009/0011)
build-serial-fix/zephyr/zephyr.elf
md5 dd56e8fe
Test harness
/tmp/hfm-verify/ (scripts + prebuilts)
two_qemu_smoke.py
Launcher
launch_openbmc.sh / launch_hfm.sh
cold-boot auto-discovery
QEMU writes the .mtd back in place — restore the pristine image from .mtd.gz before every run.
Hardware Fault Management · RAS API · MCTP/PLDM over QEMU
6

## Slide 7
LIVE DEMO · SETUP
Three SSH terminals — watch each boot yourself
Terminal 1
OpenBMC QEMU
socket server · start first
cd /tmp/hfm-verify/scripts
./launch_openbmc.sh
# press Enter, watch
# AST2600 boot -> login:
Terminal 2
Zephyr QEMU
socket client
cd /tmp/hfm-verify/scripts
./launch_hfm.sh
# press Enter, watch
# boot + reverse probe
Terminal 3
Drive PLDM
observe auto-route + forward
cd /tmp/hfm-verify/scripts
./drive_bmc_pldm.sh
# auto-discovered route
# forward pldmtool
Order matters: T1 (server) → T2 (client) → T3 (after BMC shows the login banner). All three SSH to the same dev host.
Hardware Fault Management · RAS API · MCTP/PLDM over QEMU
7

## Slide 8
LIVE DEMO · STEP 1-2
Boot both QEMUs — the part you can now SEE
Terminal 1 — OpenBMC (AST2600)
./launch_openbmc.sh
<Enter>
...U-Boot / kernel / systemd...
evb-ast2600 login:
• Full AST2600 boot is visible (was hidden by the one-shot script).
• 2nd UART (ttyS0) is exported as the MCTP socket server.
• Console login root / 0penBmc (T3 uses SSH, no manual login).
Terminal 2 — Zephyr (RISC-V)
./launch_hfm.sh <Enter>
*** Booting Zephyr OS v4.3.0 ***
serial_bridge: EID 18 ... ready
BMC GetTID try 1 rc=-116, retrying
^ retries until mctpd auto-discovers
• Zephyr = EID 18: PLDM Type 0/2 + MCTP control responder.
• Its requester thread probes the BMC and retries (-116) —
normal until mctpd finishes auto-discovery (SetupEndpoint).
• Then the reverse probe completes on its own — watch here.
Hardware Fault Management · RAS API · MCTP/PLDM over QEMU
8

## Slide 9
LIVE DEMO · STEP 3 (Terminal 3)
Forward path — BMC discovers & polls Zephyr
BMC# mctp route # installed by mctpd, not by hand
eid min 18 max 18 net 1 dev mctpserial0 mtu 68
BMC# pldmtool base GetTID -m 18
GetTID rc=0 → Response: 1
BMC# pldmtool base GetPLDMTypes -m 18
GetPLDMTypes rc=0 → base(0) + platform(2)
BMC# pldmtool platform GetPDR -m 18 -d 0
Terminus Locator PDR, recordHandle 1, TID 1, EID 18
BMC# pldmtool platform GetSensorReading -m 18 -i 1 --rearm 0
presentReading 31, Sensor Enabled, Sensor Normal
mctpd auto-installed the EID-18 route (no manual route add); drive_bmc_pldm.sh then polls over the REAL kernel AF_MCTP stack.
Point out: GetPDR returns a real Terminus Locator PDR and the sensor reading (die-temp = 31°C) — this is Hardware Fault Management telemetry actually flowing over the wire.
Hardware Fault Management · RAS API · MCTP/PLDM over QEMU
9

## Slide 10
LIVE DEMO · STEP 4 (watch Terminal 2)
Reverse path — Zephyr → BMC (patch 0009)
The bug (before 0009)
Zephyr requester sent with the MCTP tag-owner (TO) bit = 0.
Linux AF_MCTP delivers an inbound SOM frame to a bound socket only when TO = 1; TO = 0 is treated as an orphan response and dropped (-ENOENT).
Symptom: rx_packets grows, tx stays 0, every call -ETIMEDOUT.
The fix (patch 0009)
In pldm.c pldm_send_request_sync():
MCTP_MESSAGE_TO_DST → MCTP_MESSAGE_TO_SRC
Requester now sets TO = 1, so the kernel routes the request to the bound responder socket.
Merged in RASAPI (PR #1).
Zephyr console (answered by the stock BMC pldmd, no manual responder):
<inf> serial_bridge: BMC GetTID -> 0x01
<inf> serial_bridge: BMC GetPLDMTypes -> byte0=0x1d
<inf> serial_bridge: BMC GetPLDMVersion(BASE) -> 1.0.0
<inf> serial_bridge: Reverse-direction PLDM probe to BMC complete
Hardware Fault Management · RAS API · MCTP/PLDM over QEMU
10

## Slide 11
FULL AUTO-DISCOVERY
Three fixes that make mctpd self-discover at boot
Cold boot, zero manual steps — mctpd finds EID 18 on its own
1. Kernel (patch 0010): 6.6.92's for_each_netdev_dump() used xa_for_each_start(), whose cursor never advances at end-of-walk — so the AF_MCTP address dump (mctp_dump_addrinfo) never emits NLMSG_DONE and mctpd spins at 100% CPU. Backport upstream cfa7fa02078d.
2. Zephyr control responder (patch 0011): control replies wrongly set TO = 1; the BMC kernel treats them as new requests and the mctpd physical-addressing discovery query times out. Reply with TO = 0.
3. BMC systemd order (patch 0006): mctpd snapshots the link table once at startup, so the serial link must exist first. Split into mctp-local.service (Before mctpd) + mctp-setup-endpoint.service (After mctpd).
Verified end to end on a from-recipe rebuild
✓ mctp-local → mctpd → mctp-setup-endpoint all active; SetupEndpoint succeeds, endpoints/18 published on D-Bus
✓ mctpd auto-installs the kernel route (eid 18 dev mctpserial0); forward pldmtool GetTID/PDR/Sensor all rc=0
✓ Reverse probe (patch 0009) completes on its own — answered by the stock pldmd, no manual responder
Hardware Fault Management · RAS API · MCTP/PLDM over QEMU
11

## Slide 12
RECAP
The whole demo — three terminals
1
T1: ./launch_openbmc.sh
boot OpenBMC (server) → login:
2
T2: ./launch_hfm.sh
boot Zephyr (client), watch retries
3
T3: ./drive_bmc_pldm.sh
observe auto-route + forward pldmtool
4
T3 output: GetTID/PDR/Sensor rc=0
forward path verified
5
T2 output: 'Reverse-direction ... complete'
reverse path (patch 0009)
Full presenter script with expected output & fallbacks: DEMO_GUIDE.md
Hardware Fault Management · RAS API · MCTP/PLDM over QEMU
12

## Slide 13
Questions & discussion
Hardware Fault Management RAS API — MCTP / PLDM over QEMU
Repo: OCP-China-Projects/Hardware-Fault-Management · branch RASAPI
Design: docs/pldm-mctp-i3c-design.md · Build: README.md · Patches: patches/README.md
Demo host: internal dev machine · Presenter guide: DEMO_GUIDE.md